## Slide 1: Owl Robot
Anhar Risnumawan

## Slide 2: Owl Robot Overview
Nodding motion
Vibrate
Owl hooting sound

## Slide 3: Stacked Hardware
Speaker and amplifier (Left)
Battery, servo motor, mini vibration motor (Middle)
Main controller: m5stamp c3u, timer power module, and other circuitries (Right)

## Slide 4
Electrical Diagram

## Slide 5: Top Layer
Pin from top-to-bottom
Mini vibration motor
  Power motor +3.7v
  Power motor –
Lipo Battery
  +3.7v
  -
Servo
  -
  +5v
  Pwm
Speaker
  -
  +5v
  Not used
  LRC
  BCLK
  DIN
Upload
Program
USB type C
For Charging
Power
Reset
Power Switch
Mini Vibration
Motor
LiPo Battery
Speaker
Servo

## Slide 6: Top Layer
PCB connection
Resistor
Divider
Motor Control

## Slide 7: Middle Layer
Battery, servo motor, mini vibration motor

## Slide 8: Bottom Layer
Speaker and amplifier
3d printed part

## Slide 9: Troubleshooting
There is a noise from the speaker that is caused by the boost converter
Add several capacitors in the battery input and bat_out pins of the timer power module
Motor vibration should not be turned on for a long time. This can cause battery drop affecting boosting to 5v

## Slide 11: Add Filter Capacitors

## Slide 12: Test
Speaker is working
Vibration is working
The servo is working, but a string is still not connected to the owl’s head.
Battery cables still have to clear up
Probably add two Li-po batteries in parallel
The charging port is a bit blocked by the headstand

## Slide 13: Function Expansion Tree-like Structure

## Slide 14: Scenario
This owl will be put in the entrance of a trailing living life
This is when the weight, height, and face of a person are recorded
Therefore, add a small Nuc to add a speaker and a camera

## Slide 15: Test 2
Change the wire to the head
The wire connects servo motor to the head for nodding motion

## Slide 16: HTTP Control Process for Owl Robot